## Slide 1: Embedded Stereo Vision
Rahul Bhartari
Autonomous Vehicles Engineer

## Slide 2: Object Detection and Tracking for ADAS
In next generation vehicles, Emergency Brake Assist and Automatic Braking System will be crucial components of Advanced Driver Assistance Systems (ADAS). These systems need an object detection and tracking system for efficient functioning due to highly unpredictable traffic in India. At the same time, cost of the system must be low enough to make it a viable product.
Figure 2: Object detection on Indian roads dataset
Source: https://factordaily.com/india-driving-dataset-iiit-hyderabad/
Figure 1: Chaotic situation of traffic on Indian roads
Source: https://www.indiandrives.com/tag/tips-for-driving-on-indian-roads/

## Slide 3: My role in proposed system
Role : R&D for Stereo algorithm development
Left Camera
Right Camera
Source: https://www.youtube.com/watch?v=bdLL73ZHdak
Stereo Camera
Stereo Disparity Calculation
Object Detection
Disparity Clustering
Object Tracking
Collision Warning
Vehicle Control System
Figure 3: Proposed System which needs to be run on a low cost and low power ARM SOCs
Real Time Object Detection and Tracking using Stereo Vision
Calibrated Images

## Slide 4: Stereo Vision
Stereo Vision refers to extraction of 3D information from two images taken by two horizontally displaced cameras by finding correspondence between pixels in these images.
Figure 4: Two cameras taking picture of a scene from different points of view.
Source: Wikipedia
Disparity is the horizontal displacement in position of an object in the source and target images.
Stereo Correspondence Algorithms
Local:
Semi-Global Matching (OpenCV)
Semi-Global Block Matching (OpenCV)
Fast Segment Based Stereo
Adaptive Support Weights
Fast Bilateral Stereo
Global:
Stereo matching using Graph cuts
Stereo matching using Belief Propagation

## Slide 5: Fast Bilateral Stereo algorithm
Where,
is mean of pixels in the square block
is standard deviation for the block
is the block size
u, v is current pixel’s x-y index
d is disparity where NCC is calculation
n is the number of pixels in the block
(2 +1)
Implemented Normalised Cross-Correlation for cost calculation because it works independently of different lighting in left and right scenes.
Figure 5: Fast Bilateral Stereo stages
Source: https://arxiv.org/pdf/1807.01874
Cost calculation: NCC

## Slide 6: Aggregation using Locally Consistent Stereo
Where and are empirically derived.
Implemented an aggregation technique defining a plausibility function that captures the geometric and photometric constraints and independently enforcing within the neighboring pixels.
Figure 6: Central pixel ‘f’ and supporting pixel ‘g’ in reference and target images.
Figure 7: Pixels in the reference image block supporting the disparity assumption.
Support probability calculation
Figure 8: The same red point is included by the supports deployed to determine the correspondences of different blue points.
Source: https://ieeexplore.ieee.org/document/5457496

## Slide 7: Compute Optimization
Heterogeneous
Multi-threading
Full fledged stereo matching disparity calculation is a compute intensive process, especially when working with huge cost volumes.
Thread 1
Thread 2
Thread 3
Thread 4
Image divided into multiple parts for parallel processing
Cost is calculated only for 3 out of 5 pixels
Summed area table.
Source: Wikipedia
Compute Optimizations
Loop Unrolling
SIMD
Sparse Computations
Figure 9: Different techniques used for compute optimizations resulting in better performance.
Pipelined Execution
Avoid extra computations
Ensures max efficiency

## Slide 8: Memory Optimizations for performance
Stereo Vision demands a lot of memory if done in usual manner. 3D Cost volumes cost a lot in terms of memory at higher resolutions. Accessing such huge memory can create performance bottlenecks.
Memory Optimizations
Memory design for easy vectorization
Data Type Selection
Improves Cache hits
Reduces overall required memory
One Time Allocation
Lookup Tables
Figure 10: Different techniques used for memory optimizations resulting in low memory consumption with better performance.
Image Resolution | 640x480
Disparity Levels | 144 pixels
Data type for values | 32-bit Float
Memory required | 169 MB
Memory Required for single NCC Cost volume
No memory leaks
Table 1: Memory required for NCC cost volume.
Memory requirement becomes almost its 5 times for a 720p image.
Quick access

## Slide 9: Results
Normalised cross-correlation as cost function, produces good results even when used without any aggregation stage.
Figure 12: Output disparity map generated using NCC as cost.
Figure 11: Input left(top) and right(bottom) camera images.

## Slide 10: Results
Locally consistent stereo aggregation significantly improved the quality of disparity map.
Improvements Achieved | Intel Core i7 @4.2GHz | ARM Cortex A72 @1.9GHz
Loop Unrolling | 500% | 500%
Memory Optimizations | 15-20% | 15-20%
Multi-threading (2-threads) | 200% | 200%
Sparse Computations | 30 - 40% | 0%
Table 2: Improvements in disparity calculation on Intel and ARM CPUs as compared to code which does not use the mentioned techniques.
Figure 12: NCC+LC disparity map.

## Slide 11: Stereo Depth Perception Video Pipeline
This is a unique pipeline for stereo video stream processing, which can save a lot of computation and memory.
Stereo Images @720p
Stage 1: NCC only
Resize to 240p
Disparity Upsampling to 720p
Scheduler
Stage 2: NCC + LC
Post Processing
Output Disparity Map
Figure 13: Pipeline for processing stereo video stream.

## Slide 12: Work in progress ...
Tasks to be completed:
Stereo video pipeline
Pipeline testing on ARM
This project can be further improved by:
Using OpenCL for using ARM Mali GPU for computations.
Using NEON intrinsics or ARM Compute Library.
Stereo video pipeline can save approximately 84% of computations and memory required.

## Slide 13: Thank You